## Slide 1: 1. Why does the present VLSI circuits use MOSFET’s instead of BJT’s?

## Slide 2: 2. What is the need for power reduction?

## Slide 3: 3. What is the major source of power wastage in SRAM?

## Slide 4: 4. Does software play any role in low power design?

## Slide 5: 5. Give some low power design techniques?

## Slide 6: 6. What is mean by dynamic hazard?
A dynamic hazard is the possibility of an output changing more than once as a result of a single input change. Dynamic hazards often occur in larger logic circuits where there are different routes to the output (from the input). If each route has a different delay, then it quickly becomes clear that there is the potential for changing output values that differ from the required / expected output. e.g. A logic circuit is meant to change output state from 1 to 0, but instead changes from 1 to 0 then 1 and finally rests at the correct value 0. This is a dynamic hazard. As a rule, dynamic hazards are more complex to resolve, but note that if all static hazards have been eliminated from a circuit, then dynamic hazards cannot occur.

## Slide 7: 7. What is mean by static hazard?
A static hazard is the situation where, when one input variable changes, the output changes momentarily before stabilizing to the correct value. There are two types of static hazards:
Static-1 Hazard: the output is currently 1 and after the inputs change, the output momentarily changes to 0 before settling on 1
Static-0 Hazard: the output is currently 0 and after the inputs change, the output momentarily changes to 1 before settling on 0

## Slide 8: 8. Why is NAND gate preferred over NOR gate for fabrication?
NAND is a better gate for design than NOR because at the transistor level the mobility of electrons is normally three times that of holes compared to NOR and thus the NAND is a faster gate. Additionally, the gate-leakage in NAND structures is much lower. If you consider t_phl and t_plh delays you will find that it is more symmetric in case of NAND ( the delay profile), but for NOR, one delay is much higher than the other(obviously t_plh is higher since the higher resistance p mos's are in series connection which again increases the resistance).

## Slide 9: 9. What are the limitations in increasing the power supply to reduce delay?
The delay can be reduced by increasing the power supply but if we do so the heating effect comes because of excessive power, to compensate this we have to increase the die size which is not practical.

## Slide 10: 10. What is metastability? When/why it will occur? Different ways to avoid this?
Metastable state: A un-known state in between the two logical known states. This will happen if the O/P cap is not allowed to charge/discharge fully to the required logical levels. One of the cases is: If there is a setup time violation, metastability will occur, To avoid this, a series of FFs is used (normally 2 or 3) which will remove the intermediate states.

## Slide 11: Answer these questions
1. what is the difference between latch and flip-flop?
2. what is latchup?
3. what is noise margin?
4. what is body effect?
5. Which transistor has higher gain. BJT or MOS and why?